## Slide 1: Cloud iNfrastructure Telco Taskforce Reference Model – Network Model Evolution Wednesday 24th June, 2020

## Slide 2: Agenda
  Introduction
  CNTT Reference Model evolution
  CNTT RM Logical Architecture
  HW Infrastructure Manager
  CNTT RM deployment example
  Q&A

## Slide 3: Introduction – role of Reference Model (RM)
Reference Conformance
Reference Implementation
Reference Model
Framework Requirement
TC High Level Definitions &
Traceability to Requirements
Playbook
Reference Architecture
Installers Requirements
Lab Req &
Playbook
Installation Playbook
Specification
Specification
RM provides technology agnostic directions for the CNTT Cloud Infrastructure specifications in Reference Architectures (RAs), and consequently in RIs and RCs
RM provides technology agnostic CNTT requirements for VNF/CNF vendors to guide them in their design of network applications
GSMA is an ultimate owner of CNTT Reference Model, and as such RM is a window into the CNTT work for a wider telco community

## Slide 4: Introduction – RM overall goal and approach
Our goal: normalization of integration reference points between different layers of the Cloud Infrastructure architecture stack, e.g. packet flow and control flow interfaces between Virtualization level (be it IaaS or CaaS type of virtualisation) and Networking Hardware resources, and related integration into MANO level.
Our approach: to ensure the ability for supporting simultaneous usage of different CNTT reference architectures by having multiple CaaS and IaaS layers using shared Hardware Infrastructure layer.

## Slide 5: CNNT Reference Model “1.0” vs Baraque Release needs
Cloud Infrastructure
Physical resources
Virtual resources
Management software
VNFs/CNFs
Management client
Consumes virtual resources
Manages virtual resources
RM Baraque Rel focus
Networking Modelling
Networking & Storage Characterization
Full Containerization support
HW Acceleration support.
Reference Model needs to evolve to cater for the features needed for the Baraque Release and beyond…

## Slide 6: Identified key areas of concern in RM “1.0”
Need to recognise separation between management of hardware infrastructure and virtual infrastructure (e.g. containers and VMs)
Need to define in detail reference points between the Virtual Infrastructure Layers and the Hardware Infrastructure Layer
Need to abstract hardware resources towards Virtual Infrastructure Layers and above (VNFs, CNFs) hiding hardware deployment details.
  Note: Lack of this definition often causes problems with portability, and impairs standardization of technologies such as acceleration and encapsulation
Need to specify in detail references to SDN in the Cloud Infrastructure context
Need to address how RM/RAs will enable utilization of programmable forwarding planes in HW layer

## Slide 7: CNTT Reference Model “2.0” - across HW / IaaS and CaaS
Management clients
Container Infrastructure Service Instance
Hypervisor
Compute Resources
Storage Resources
Network Resources
Container Infrastructure Service Manager
Virtual Infrastructure
Manager
Hardware Infrastructure
Manager
SDN3
SDN1
SDN2
Cloud Infrastructure
Hardware
Infrastructure
Layer
Virtual
Infrastructure
Layer
Management software
Resources
Consume
virtual
resources
Manage
virtual
resources
VM
VM
VM
Container Infrastructure Service Instance
VM
VNFs
CNFs
CNFs
Consume
virtual
resources
Consume
virtual
resources
Virtual Resources
Hardware Resources
Manage
HW
resources
Bare metal
Containers
Containers

## Slide 8: CNTT RM Logical Architecture
VM
Cloud Infrastructure
Container Infrastructure Service Instance
(CaaS on Bare Metal)
Container Infrastructure Service Instance
(CaaS on IaaS)
Storage Resource
Network Resource
CNF
CNF
Virtual Machine Manager
(IaaS Hypervisor)
HW Resource Pool
VNF
Virtual Infrastructure Manager
HW Infrastructure Manager
Orchestrator(s)
OSS/BSS
Vl-Ha
Vn-Nf
Vl-Ha
VNF Manager
HW Equipment
Management
Nf-Vi
ETSI NFV reference point
Non-CNTT reference point
Compute Resource 1
Compute Resource m
Management and Orchestration
Container Infrastructure Service Manager
Hardware Infrastructure Layer
Virtual Infrastructure Layer
HW Infrastructure
Management
Vn-Nf
SDNu
SDNu
SDNo
SDNo
ContainerRT +SecNW
Container Management
Container
Container
VM
CNTT reference point
Vi-Vnfm
Or-Vnfm
Virtual Infrastructure
Management
HW Resource Management
HW Status/Provisioning/Fulfillment

## Slide 9: HW Infrastructure Manager characteristics
HW Infrastructure Manager is a logical block of functionality
  Is the provisioning manager for abstracted HW Resources
    Compute, Storage & Network
  Is the authoritative manager for the physical HW resources
  It can be accessed by multiple different authorized actors
  Functions can be implement centralized and distributed
    e.g. on the managed equipment
  Is shielded from Composed Server Host software direct involvement

## Slide 10: HW Infrastructure Manager key functions
Equipment Asset and Physical Topology Discovery
HW Infrastructure Management Addressing, Topology and Authorization
Equipment Firmware management
Equipment Fault management
HW Infrastructure Telemetry and Log collection and services
HW Resource Composition, i.e. Creation of abstracted HW Resources - Compute, Storage & Network
Underlay Network Management
  Switch Fabric & SmartNIC management
  HW Resource Composition network management
  Overlay Network services e.g. VTEP terminations, Selective monitoring and Tapping
Emergency and console connectivity management
Basic Storage Device, Block, Volume and Topology management
HW Accelerator services
Boot services e.g. for accelerators, switches, composed servers

## Slide 11: CNTT RM deployment example
VM
IaaS Virtualization Instance (VMM)
Cloud Infrastructure
CaaS Virtualization Instance n (CISI)
CaaS Virtualization Instance 2 (CISI)
Storage Resource
Network Resource
Virtual Computing
Virtual Storage
Virtual Networking
CNF 2:1
VNF 1:1
Virtual Computing
Virtual Storage
Virtual Networking
HW Infrastructure Layer Resource Pool with HW Layer Abstraction
CNF n:1
CNF 2:2
VNF 1:2
CNF n:2
CNF 2:3
VNF 1:3
CNF n:3
VIMV1
CISM C2
CISM Cn
HW Infrastructure Manager
Orchestrator
1
OSS/BSS
Vn-Nf
Os-Ma
Vl-Ha
C-RT + SecNW
Vn-Nf
Vn-Nf
PacketFlow
Vl-Ha
CNF Mgr2
CNF Mgrn
VNF Mgr1
Or-Vnfm
Or-Vnfm
Or-Vnfm
Vi-Vnfm
HW Equipment Management
Container & NW Management
Nf-Vi
ETSI NFV reference point
Other reference point
Execution reference point
Each colors represents a separate administrative domain
Compute Resource 1
Compute Resource m
C&NW Mgmt
Virtual Computing
Virtual Storage
Virtual Networking
PacketFlow
PacketFlow
Packet Flow interface
SDNu -V1
SDNu -Cn
SDNu Provisioning
HW Infra Mgmt
Orchestrator
n
Vn-Nf
SDNu -C2
SDNo -V1
CNI SDN
Container
C-RT + SecNW
C-RT + SecNW
Container
Container
C-RT + SecNW
Container
C-RT + SecNW
Container
C-RT + SecNW
Container
VM
VM
VM
CNTT reference point
HW Resource Management
Virtual Infra Mgmt

## Slide 12: Q&A