## Slide 1
China Mobile
SHASHA GUO，YING LI
Cyborg Acceleration Management

## Slide 2: Agenda
Cyborg Acceleration Management
Cyborg Enhancement requirements for CNTT

## Slide 3
Why we need cyborg acceleration management
不同场景下加速卡管理分析
Network card
Nic driver
Acc hardware 2
Acceleration hardware 1 driver
Acceleration hardware 2 driver
Acc hardware 1
Nic driver
Acceleration hardware 1 driver
Acceleration hardware 2 driver
VNF APP
Method 1: NOVA management-common network card management
Principle: When the virtual layer (cloud platform) is installed and deployed, the deployment worker writes the number of accelerated network cards (of the same standardized function) and the correspondence between the accelerated network card and the PCI interface in the configuration file, and NOVA is responsible for scheduling and allocating PCI.
Advantages: NOVA is now supported
defect:
NOVA does not have the function of automatically discovering resources. You need to manually configure the corresponding files before the installation and deployment of the virtual layer, and you need to restart after each configuration update to take effect.
Only applicable if the network card is of the same function type
Adaptation: The acceleration capability required by the VM indicated in the VNFD is required
Scenario description 1: In the same resource pool, the server has a network card with the same GTP offload acceleration function established by the China Mobile Standard. Problems in this scenario are accelerated card management

## Slide 4
Why we need cyborg acceleration management
不同场景下加速卡管理分析
网卡
Nic driver
加速硬件2
Acceleration hardware 1 driver
Acceleration hardware 2 driver
加速硬件1
Nic driver
Acceleration hardware 1 driver
Acceleration hardware 2 driver
VNF APP
Method 2: Cyborg Management-Accelerate hardware specific management
Principle: Cyborg component management, automatic management of accelerator cards, and cyborg component conductor dispatched to VMs.
Advantages: Mainly oriented to different types of accelerator card management and scheduling, suitable for both single-function accelerator card deployment scenarios and multi-function accelerator card hybrid deployment scenarios
Defects: the current function is not perfect, you need to mature to use
Adaptation: The acceleration capability required by the VM indicated in the VNFD is required

## Slide 5
Why we need cyborg acceleration management
不同场景下加速卡管理分析
网卡
Nic driver
加速硬件2
Acceleration hardware 1 driver
Acceleration hardware 2 driver
加速硬件1
Nic driver
Acceleration hardware 1 driver
Acceleration hardware 2 driver
VNF APP
Method: Cyborg Management-Accelerated hardware-specific management method
Principle: Cyborg component management, automatic management of accelerator cards, and cyborg component conductor dispatched to VMs.
Advantages: Mainly oriented to different types of accelerator card management and scheduling, suitable for both single-function accelerator card deployment scenarios and multi-function accelerator card hybrid deployment scenarios
Defects: the current function is not perfect, you need to mature to use
Adaptation: The acceleration capability required by the VM indicated in the VNFD is required
Scenario description 2: In the same resource pool, the server has network cards with different acceleration functions developed by the China Mobile Standards. In this scenario, the problem is accelerated card management

## Slide 6: Agenda
Cyborg Acceleration Management
Cyborg Enhancement requirements for CNTT

## Slide 7
Cyborg Enhancement requirements for CNTT
VNF
NFVO
VIM
Hardware Device
Device
VNF
VNFM
OVS Smartnic
Cyborg-agent
OVS
driver
Cyborg
Server A
FPGA Smartnic
Server B
GPU
Server C
FPGA driver
GPU driver
Hypervisor
UPF
AI/AR/VR app
1
3
2
Three issues should be taken attention:
1.Hardware selection
2.Development work
3.Acceleration resources orchestresion-Openstack Cyborg
Notes: 1. Acceleration hardware selection: select the universal acceleration hardware, formulate the standardization specification of acceleration hardware, and realize the call and acceleration resource pooling of different manufacturers.
2.According to the selection of acceleration hardware, the application is developed accordingly.
3.Accelerate resource choreography to ensure that appropriate accelerated resources can be seen and selected for VNF use through NFVO and VIM. OpenStack Cyborg currently provides some functionality

## Slide 8
Accelerated resource configuration properties | Parameter effect
PGPU attribute（call it in flavor）： resources:PGPU=N trait:CUSTOM_PGPU_<VENDOR_ID>=required trait:CUSTOM_PGPU_<PRODUCT_ID>=required trait:CUSTOM_PGPU_<PRODUCTID_VER>=required | Number of physical GPUs to be allocated, manufacturer ID or name (optional), product ID or name (optional), product version (optional)
vGPU attribute（call it in flavor）： resources:VGPU=N trait:CUSTOM_VGPU_<VENDOR_ID>=required trait:CUSTOM_VGPU_<PRODUCT_ID>=required trait:CUSTOM_VGPU_<PRODUCTID_VER>=required | Number of virtual GPUs to be allocated, manufacturer ID or name (optional), product ID or name (optional), product version (optional)
FGPA attribute（call it in flavor）： resources:FPGA=N trait:CUSTOM_FPGA_<VENDOR_ID>=required trait:CUSTOM_FPGA_<PRODUCT_ID>=required trait:CUSTOM_FPGA_<PRODUCTID_VER>=required accel:bitstream_id=<The image ID> | Number of FGPAs to be allocated, manufacturer ID or name (optional), product ID or name (optional), product version (optional), mirror image to be downloaded.
虚拟层需支持根据以下加速资源配置属性（Cyborg Device Profile Group中的Dictionaries）进行节点调度，管理编排器在创建虚拟机时根据业务的需求，配置合适的属性及数值：
Cyborg Enhancement requirements for CNTT
We recommend using Cyborg 2.0 for acceleration from the OpenStack U version. The following requirements are to meet the decoupling requirements of the NFVO and NFVI layers, to ensure that third-party manufacturers NFVO can use accelerated resources with Cyborg API v2.0:
The virtualization layer needs to support node scheduling based on the following accelerated resource configuration attributes (Dictionaries in Cyborg Device Profile Group), and the management orchestrator configures appropriate attributes and values according to business needs when creating virtual machines:
Notes: There are many options for accelerating chips in the market, and it is difficult for a single accelerating chip to meet the complex and diverse acceleration scenarios. Therefore, it is necessary to comprehensively consider the business requirements, chip capabilities, industrial maturity and power consumption of accelerating chips, and select suitable accelerThere are many options for accelerating chips in the market, and it is difficult for a single accelerating chip to meet the complex and diverse acceleration scenarios. Therefore, it is necessary to comprehensively consider the business requirements, chip capabilities, industrial maturity and power consumption of accelerating chips, and select suitable accelerating chips to achieve better acceleration effect.ating chips to achieve better acceleration effect.

## Slide 9
Q&A
guoshasha@chinamobile.com