## Slide 1
Transport Slicing Demo of Guilin
Henry Yu
Jun Sun
Hesam Rahimi
Decheng Zhang
Christopher Janz
Lin Meng
@twitter

## Slide 2: E2E Network Slicing on ONAP
Core Slice Subnet
RU
DU
CU
Core
Front Haul
Mid Haul
Back Haul
TN
TN
TN
NSMF
RAN NSSMF
TN NSSMF
Transport Slice Subnet 1
Transport Slice Subnet 2
Transport Slice Subnet 3
ONAP
Transport Network Configurations
Align with O-RAN
Core NSSMF
3rd Party
RAN NSSMF
Configure RU, DU, CU
RAN Slice Subnet
CSMF
Align with 3GPP
Align with 3GPP
Align with IETF and ZSM

## Slide 3: Scope of this Demo
Core Slice Subnet
Core Slice Subnet
RU
DU
CU
Core
Front Haul
Mid Haul
Back Haul
TN
TN
TN
NSMF
RAN NSSMF
TN NSSMF
Transport Slice Subnet 1
Transport Slice Subnet 2
Transport Slice Subnet 3
ONAP
Transport Network Configurations
Core NSSMF
3rd Party
RAN NSSMF
Configure RU, DU, CU
RAN Slice Subnet
CSMF
Demo
Transport slicing solution needs to be:
X-haul agnostic
Consumer agnostic
Self-contained and deployable
Federated solution

## Slide 4: TN Management Domain (ETSI ZSM)
Implementing transport slicing as a management domain (source: ZSM 003)
ZSM Management Domain is an architectural solution that satisfies our design requirements
Management Domain: “A scope of management that federates together management services, that enables their exposure towards external service consumers, and that is delineated by a business, administrative, technological or other boundary”.
Our transport slicing solution is implemented as a Management Domain (i.e., TN MD).

## Slide 5: Demo Setup (ONAP + Testing Tools)
ONAP
(Transport Slicing)
ACTN PNC
Simulator (A)
ACTN Topo Generator
ACTN Network
Viewer
ACTN MPI
ONAP-SO API
ACTN PNC
Simulator (B)
ACTN MPI
Domain A
Domain B
In addition to the development on ONAP, we also developed a few testing tools to facilitate testing and demo:
ACTN Topo Generator: Design and generate network topology for a particular domain. The generated topology uses the ACTN TE-topology model, and is loaded onto the ACTN PNC simulator.
ACTN PNC Simulator: Simulates transport network domain controller, which interacts with ONAP to deliver transport slicing operations.
ACTN Network Viewer: Visualizes the transport slice configurations. And also simulates TN NSSMF adapter payloads and sends them to TN NSSMF on the SO.
ACTN MPI
ACTN MPI
1
2
3

## Slide 6: What We Demo
ACTN Network Viewer
Optical domain controller simulator
Enhanced ACTN MPI
1
OTN/DWDM
OTN/DWDM
NNI
UNI
UNI
ONAP
Optical domain controller simulator
TN Management Domain
Management Functions
2
TN MD NBI provides a transport slice definition model based on an IETF draft. It also defines four TN NSSI operations: Allocate, Activate, Deactivate, and Deallocate.
Enhanced ACTN MPI: OTN slice creation RPC, EPL/EVPL model for transport slices, and OTN tunnel service model for transport slices
Network configuration data are retrieved from domain controllers and displayed in the ACTN Network Viewer.
ACTN MPI
3
Allocate, activate, …
Retrieve and visualize network configuration data

## Slide 7: How Slice Definition Model Render into Realization Models
UNI
TP
TP
TTP
inter-layer-lock-id
inter-layer-lock-id
ETH TE Link
ETH Node
ETH Node
OTN Node
OTN Node
OTN TE Link
TTP
LLCL
LLCL
NNI
UNI
NNI
Te-link-attributes: reserved ODUs, available ODUs, TS bitmap, etc.
Te-link-attributes: Max BW, Avail BW, etc.
Conn-matrix
Conn-matrix
OTN TE topology
ETH node A
TTP1
TTP5
OTN TUNNEL on RED_SLICE
OTN TUNNEL on BLUE_SLICE
ETH node B
TTP2
Phy ports
Phy. ports
TTP3
TTP7
TTP6
TTP4
TTP8
OTN TE link (max BW 100G)
Unreserved bandwidth
OTN node B
OTN node A
RAN node (gNB)
CORE network node (UPF)
RAN node (gNB)
Application Endpoints
CORE network node (UPF)
Application Endpoints
Phy ports
Phy ports
RAN slice 1
Data plane (in NEs)
Control plane data models (in ONAP and domain controllers)
Management plane data models (in ONAP)
Ethernet TE topology
RAN slice 2
Logical transport interface 1
Logical transport interface 2
abstraction
abstraction
CORE slice 1
CORE slice 2
RAN NSSI (3gpp)
CN NSSI (3gpp)
TN NSSI (IETF TSCi model)
Transport Endpoint model
abstraction

## Slide 8: Conclusion and Future Work
We demonstrate the first open source 5G transport slicing solution based on ETSI ZSM and IETF/ACTN standards. Comments/feedbacks are appreciated.
We will open source the IETF/ACTN tools used in this demo (git: onap/integration/ietf-actn-tools).
Future work may focus on closed-loop automation in transport, by continuing to collaborate with ZSM and IETF.