## Slide 1: ONAP Casablanca Use Case in CMCC Lab
China Mobile: Yan Yang
Intel: Haibin Huang

## Slide 2
CMCC Lab Overview

## Slide 3: Physical Lab Overview @CMCC
DC 2
(POD2)
VIO 4.0 (Ocata)
Controller node:2
Compute nodes: 6
Hardware: R5300/E9000, 3 rack servers and 1 blade server with 6 blades
DC 1
(POD1)
Titaninum Cloud 16.10 (Mitaka),
Controller nodes:2 , Compute nodes: 9
ONAP Deployment Env
(POD3)
Titaninum Cloud R4 (Newton),
Controller nodes:2 , Compute nodes: 3
LOM Management, Admin, Private, Public networks inside
Core Switch
Leaf Switch
Leaf Switch
Firewall
OpenVPN
Server
VPN Client
Leaf Switch
Leaf Switch
ONAP Deployment Env & VNF Env
(POD5)
ONAP Deployment Env & VNF Env
(POD4)
Titaninum Cloud 16.10 (Mitaka),
Controller nodes:2 , Compute nodes: 2
Titaninum Cloud 16.10 (Mitaka),
Controller nodes:2 , Compute nodes: 2

## Slide 4: Use Case Deployment @CMCC
Casablanca
CMCC Domain :Casablanca
VDF Domain : Casablanca
vCPE
CCVPN
OS
vDHCP
OS
vAAA
OS
vBNG
OS
OS
vxxx
vGMUX
OTN Controller
(Huawei)
SD-WAN Controller
(Huawei)
Integrate with 3rd Part Specific Components
OS
vCPE
OS
vCPE
OTN Controller (ZTE)
SD-WAN Controller
(ZTE)
Integrate with 3rd Part Specific Components
(POD3)
(POD1)
(POD4)
(POD5)

## Slide 5: Key Data @CMCC
CMCC Lab key data
ONAPs ：3
Cloud ：5 windrive(4) and
Physical hardware ：73
Participating member ：8
(1)

## Slide 6
CCVNP Use Case

## Slide 7: CCVPN Overview
  CCVPN(Cross Domain and Cross Layer VPN) by ONAP Peering Orchestration Between SPs
Internet
vCPE
vCPE
uCPE
uCPE
ONAP (CMCC)
ONAP (VDF)
SOTN Controller
SD-WAN
Controller
SOTN Controller
SD-WAN
Controller
Connection（ E-Line）
UNI
UNI
Connection（ E-Line）
UNI
UNI
Site
Site
Site
Site
Notes: 首先重点介绍的是CCVPN的用例场景，这个场景是ONAP在C版本引入的一个全新的，比较完整的端到端的用例场景。目前参与的成员包括中国移动、vdf、华为、zte、风河以及vmware。因为这个场景在之前的演讲中也已经做了详细介绍，我这里只做个简单的说明。实际上CCVPN是借助ONAP的自动编排管理能力，实现跨域（SOTN+SD-WAN）跨层(L1, L2, L3)的以及跨运营商的端到端VPN业务的自动化部署和动态调整。

## Slide 8: CCVPN Network Topology
OTN
Domain B
(HW)
OTN
Domain A
(HW)
OTN
Controller
Server A
(HW)
OTN
Controller
Server B
(HW)
CMCC ONAP
OTN network
(ZTE)
OTN
Controller
Server
(ZTE)
Vodafone ONAP
uCPE
(HW)
vCPE
(HW)
uCPE
(ZTE)
vCPE
(ZTE)
SD-WAN
Controller
Server
(ZTE)
SD-WAN Controller
(HW)
Lab
GE/10GE/OTU
GE/10GE/OTU
CMCC portal
Vodafone portal
L3
L2
Notes: 那么针对社区的11月份交付的CCVPN用例场景，我们在中国移动的ONAP实验室也进行了规划。在demo的基础上，我们引入了中兴的OTN以及SD-WAN设备，用于验证ONAP C版本的CCVPN功能。
目前我们已经在开始部署C 版本的ONAP.

## Slide 9: CCVPN Test Case
OTN
Domain1
OTN
Domain2
OTN Controller
OTN Controller
CPE
ONAP(CMCC)
vGW
SD-WAN
Controller
OTN
Domain
OTN Controller
CPE
ONAP(VDF)
vGW
SD-WAN
Controller
L2 Underlay (EoODU)
Handoff
L3 VNF
L3 PNF
L2 Underlay (EoODU)
Handoff
L3 PNF
L3 VNF
CCVPN Service
Topology Discovery
Closed Loop
Service Provisioning
Notes: 在刚刚过去的9月份的ONS 欧洲峰会上，中国移动联合VDF和华为在ONS现场联合发布了CCVPN的示范应用，在LFN的展台我们通过远程连接中国移动的CCVPN实验室，现场演示了CCVPN的三个功能场景，包括网络拓扑发现、服务提供以及闭环自愈的场景。

## Slide 10
vCPE Use Case

## Slide 11: vCPE Test Case
Model Design
Service Deployment
Service Recovery
VNF Onboarding
NS Design
Instantiation
Termination
VM shutdown
Triger Healing
CPE
Healing
CPE
vCPE NS
VNF Instantiation
vGRE
vINFRA
vBNG
vGW
vGMUX
VNF Destruction
ESR Registration
Vim Registration
VNFM Registration
Key Test Case: ESR Registration, Model Design, Service Deployment, Service Recovery
Notes: 另外要提到的一个端到端的应用场景是vCPE的场景，目前vCPE的场景在ONAP社区有两种部署方式，一种是通过HEAT模版，一种是通过Tosca模板。ONAP C版本的HEAT模型主要用于一系列回归测试，Tosca-based vCPE 在上一个Beijing版本我们做个初步尝试，但由于SDC对tosca模型支持的限制，没有完成端到端的测试。那么这个版本，我们在中移的ONAP实验室会继续端到端的验证测试，最终的Tosca-based的vCPE主要基于VFC 的gvnfm来进行部署，同时我们叠加了硬件能力发现HPA的功能。

## Slide 12: vCPE – Overall Sequence
Design Time
Run Time
Notes: VF-C aligns with R2 VNF data model in Beijing Release. In addition to supporting VoLTE use case, VF-C also supports CPE use case which integrates with open source VNF via GVNFM in Beijing release.

## Slide 13
Design Time

## Slide 14: vCPE – Package Design & Distribution
GW\BNG\...
CPE NS
VFC
VNF Package
CPE E2E
SDC
SO
NS Package
Service Package
Catalog
Usecase UI
1.VNF Package Upload
vCPE E2E Service Package
NS/VNFs Package
Policy
3.Service Package Design
2.NS Package Design
5.NS/VNF Pkg Distribution
4.1 E2E Service Pkg Distribution
4.2 E2E Service Pkg Distribution
4.3 Query VNF Pkg
4.4 Query NS Pkg
Notes: VF-C aligns with R2 VNF data model in Beijing Release. In addition to supporting VoLTE use case, VF-C also supports CPE use case which integrates with open source VNF via GVNFM in Beijing release.

## Slide 15: vCPE – Package Design & Distribution
VNF Package Onboarding in UUI
NS Package Onboarding in UUI
NS Design in SDC
Notes: VF-C aligns with R2 VNF data model in Beijing Release. In addition to supporting VoLTE use case, VF-C also supports CPE use case which integrates with open source VNF via GVNFM in Beijing release.

## Slide 16
ESR Registration

## Slide 17: VIM Configuration
10
NIC configure
We can refer to [1] before “Launching instances with SR-IOV ports”
pci_passthrough_whitelist = { "devname": "eth3", "physical_network": "physnet2"}
Create aggregate
$ openstack aggregate create --property sriov_nic=sriov-nic-intel-1234-5678-physnet1:1 aggr11
Create flavor
$ openstack flavor create onap.flavor1 --id auto --ram 512 --disk 40 --vcpus 4
$ openstack flavor set onap.flavor1 --property sriov_nic=sriov-nic-intel-1234-5678-physnet1:1
Create provider network

## Slide 18: MultiCloud register and HPA discovery

## Slide 19: VIM & GVNFM Registration via ESR GUI
VIM Registration
GVNFM Registration

## Slide 20: AAI information
10
sriov_nic=sriov-nic-<vendor>-<Vendor ID>-<Device ID>-<physicalNetwork:COUNT>
It is expected thatOpenstackadministrator creates alias that stars with sriov and put the vendor ID, device ID.
Example:
Assume that there are two SRIOV-NIC cards supported by a region, Intel and Mellanox.
sriov-nic-intel-1234-5678-physnet1:1
sriov-nic-mellanox-2345-6543-physnet1:1

## Slide 21
Run Time

## Slide 22: ONAP – Run Time
Lifecycle: Instantiate/terminate/heal…
UUI
VF-C
Multi-Cloud
WindRiver
(Openstack)
1
4
3
5
OOF
Policy
2

## Slide 23: Policy
Policy
Policy Driven Decision & Enforcement Framework
Customer
Input
Policy DB
Policy Distribution
REST APIs/Event Driven
OOF
Policy Creation
Administration
SDC
"flavorLabel":"vcpe.vgw",
"flavorProperties":[{
"hpa-feature": "sriovNICNetwork",
"mandatory": "True",
"architecture": "generic",
"hpa-version": "v1",
"directives" : [
{
"type": "sriovNICNetwork_directives",
"attributes": [
{"attribute_name": "vgw_nic_type", "attribute_value": “direct"},
{"attribute_name": "vgw_provider_network", "attribute_value": “physnet1"}
]
}
],
"hpa-feature-attributes": [
{
"hpa-attribute-key": "pciVendorId",
"hpa-attribute-value": "1234", "operator": "=", "unit": ""
},
{
"hpa-attribute-key": "pciDeviceId",
"hpa-attribute-value": "5678", "operator": "=", "unit": ""
},
{
"hpa-attribute-key": "pciCount",
"hpa-attribute-value": "1", "operator": ">=", "unit": ""
},
{
"hpa-attribute-key": "physicalNetwork",
"hpa-attribute-value": "physnet1", "operator": "=", "unit": "“
}
]
},
]
REST APIs

## Slide 24: VF-C — OOF Homing
VFC sends out homing request to OOF(OSDF) containing resource info
OOF(OSDF) pulls all the related homing constraints from Policy
OOF(HAS) check AAI database to pull region(flavor) information
OOF(OSDF) returns homing allocation solution to VFC
VFC
Policy
OOF - HAS
AAI
①
②
③
④
OOF- OSDF
OOF: ONAP Optimization Framework
OSDF: Optimization Service Design Framework
HAS: Homing Allocation Service

## Slide 25: OOF Homing
"flavorLabel":"vcpe.vgw",
"flavorProperties":[{
"hpa-feature": "sriovNICNetwork",
"mandatory": "True",
"architecture": "generic",
"hpa-version": "v1",
"directives" : [
{
"type": "sriovNICNetwork_directives",
"attributes": [
{"attribute_name": “vgw_vnic_type", "attribute_value": "direct"},
{"attribute_name": “vgw_provider_network", "attribute_value": "physnet1"}
]
}
],
"hpa-feature-attributes": [
{
"hpa-attribute-key": "pciVendorId",
"hpa-attribute-value": "1234", "operator": "=", "unit": ""
},
{
"hpa-attribute-key": "pciDeviceId",
"hpa-attribute-value": "5678", "operator": "=", "unit": ""
},
{
"hpa-attribute-key": "pciCount",
"hpa-attribute-value": "1", "operator": ">=", "unit": ""
},
{
"hpa-attribute-key": "physicalNetwork",
"hpa-attribute-value": "physnet1", "operator": "=", "unit": "“
}
]
},
]
AAI
Policy

## Slide 26: VFC Create network and port
"type": "sriovNICNetwork_directives",
"attributes": [
{"attribute_name": “vgw_vnic_type", "attribute_value": "direct"},
{"attribute_name": “vgw_provider_network", "attribute_value": "physnet1"}
Create network, ports
# openstack network create --provider-network-type vlan --provider-physical-network physnet1 tst-network
# openstack port create --name sriov-port --binding:vnic-type direct
b. Create server
# openstack server create --flavor onap.hpa.flavor11 --image Ubuntu_16.04 --nic port-id= test-sriov-nic

## Slide 27: MultiCloud
27
ONAP
MultiCloud
Framework
Plugin-
Pike
Plugin-StarlingX
Plugin-vmware
Pike
StarlingX
vmware
Windrvier
Plugin-windriver
Other Components
SO and VFC will call Framework

## Slide 28: Thank you!

## Slide 29
Back Up

## Slide 30: vCPE - Design Time
GW
GMUX
BNG
INFRA
GW
GMUX
BNG
INFRA
BGREMU
BGREMU
VF
VNF包
Network Service
1
2
3
vCPE E2E
4
OS
vINFRA
OS
VBGREMU
OS
vBNG
OS
OS
vGW
vGMUX

## Slide 31: vCPE Test Case
HEAT
TOSCA
SO
MultiCloud
SDC
NSLCM
GVNFM
A&AI
vGMUX
vGW
vXX
vGMUX
OOF
VF-C
Tosca based vCPE in CMCC
Notes: 另外要提到的一个端到端的应用场景是vCPE的场景，目前vCPE的场景在ONAP社区有两种部署方式，一种是通过HEAT模版，一种是通过Tosca模板。ONAP C版本的HEAT模型主要用于一系列回归测试，Tosca-based vCPE 在上一个Beijing版本我们做个初步尝试，但由于SDC对tosca模型支持的限制，没有完成端到端的测试。那么这个版本，我们在中移的ONAP实验室会继续端到端的验证测试，最终的Tosca-based的vCPE主要基于VFC 的gvnfm来进行部署，同时我们叠加了硬件能力发现HPA的功能。

## Slide 32: vCPE Test Cases
Topology
vCPE
Network service
vCPE
E2E service
Service lifecycle
Management
Service Instantiation
Use GVNFM to integrate with Open source VNFs of CPE use case .
No commercial software
Model distribution
Service Termination
Service Healing
vGW
vGMUX
Public_net
Private_net
VF
VF
VL
VL
VF x
VF
VL x
VL